## Slide 1: Third Automotive CFD Workshop Case 1 Windsor Squareback at Yaw Overall Analysis
Gary Page Aeronautical & Automotive Engineering Loughborough University
Barcelona, September 2022
G.J.Page@lboro.ac.uk
Copyright: G.J.Page 2022; License: CC BY-NC 4.0

## Slide 2: Introduction
Previous workshops have used a simplified model for Case 1
Second workshop Windsor Squareback (with wheels and no wheels)
  Duplication of effort for two cases
  Bi-stability tended to obscure importance of other features
  Little benefit of ‘wall resolved’ low y+ grids/models
  Criticism that we could not understand grid sensitivity
Third workshop:
  Single case (no wheels)
  Small yaw (2.5 degree) to remove potential bi-stability
  Single baseline compulsory (g2) grid for RANS and scale resolving (37M cells)
    Coarse g1 doubled cell size (6.7M) and fine g3 almost halved cell size (198M)

## Slide 3: Windsor Squareback Model
Reference area 0.112m2, reference length 0.6375m
Origin on centreline, on floor, midway between pins

## Slide 4: Wind Tunnel and CFD domain
Experiment: a 3.2m long working section, 1.92m wide x 1.32m high cross section expanding to 1.94m wide
CFD: extend upstream and downstream to 11m long, parallel sidewalls
  No slip (or symmetry) for side walls and roof

## Slide 5: Grids
STAR-CCM+ trimmer + prism layer
Baseline (compulsory) g2 has smallest cubical cells 2.4x10-3 m
  g1 x2 4.8x10-3 m, g3 1.32x10-3 m
  6.7M, 37M and 197M
All three grids have same prism layer near well cell height, number of layers, and thickness
Same grid for RANS/DES/LES
  Should be suitable for WMLES
  DES/RANS would normally have higher aspect ratios
Aiming for near wall cell centre y+ of 40 on model and 50-75 on ground plane

## Slide 6: Grid Refinement Zones

## Slide 7: Grid Side View

## Slide 8: Near Wall Cell Centre y+

## Slide 9: Test Case
2.5 degree yaw (rotated –ve around z axis)
40 m/s , gives Re 3x106 (based on vehicle length)
Use a virtual probe ahead of model on roof [2.0,0.0,1.3]m to determine
  Reference pressure
  Reference velocity
  Use for all force and pressure coefficients
No wind tunnel corrections
All force coefficients are in the yawed vehicle coordinate system (VCS)
Symmetry and glasshouse pressure in VCS
Base pressure and PIV slices in Wind Tunnel Coordinate System (WTCS)

## Slide 10: Experimental Data
Pressure tappings along symmetry plane and glasshouse plane
Pressure tappings on base
PIV slice horizontal plane (red)
Tomographic PIV (30m/s) for volume – used to generate other experimental slices (blue, green, light blue)
https://repository.lboro.ac.uk/articles/dataset/Windsor_Body_Experimental_Aerodynamic_Dataset/13161284

## Slide 11
Results Taster…

## Slide 12: Contributions
47 calculations submitted
9 organisations
  3 Universities / Research Institutes
  1 large CFD vendor
  5 small/medium CFD vendors/consultancies
22 on standard grids, 25 on ‘own’ grids
20 RANS/URANS solutions, 27 DES/LES/LBMDES

## Slide 13: Drag Coefficient: All
Significant variability
Tend to underpredict drag

## Slide 14: Drag Coefficient: RANS and URANS, all grids
RANS and URANS much lower drag than LES/DES
Own grid
Low y+
SA and variants
SA is anomaly with high drag

## Slide 15: RANS SA Base Pressures
SA (0.3583)
SA-RC (0.3474)
SA-QCR (0.3517)
Experiment (0.3298)
CD in (brackets)

## Slide 16: RANS SA Horizontal Slice Streamwise Velocity (PIVblue)
SA (0.3583)
SA-RC (0.3474)
SA-QCR (0.3517)
Experiment (0.3298)
CD in (brackets)

## Slide 17: Drag Coefficient: RANS and URANS, all grids
RANS and URANS much lower drag than LES/DES
EARSM
SA is anomaly with high drag
EARSM has lowest drag

## Slide 18: URANS EARSM Base Pressures
EARSM g1 (0.2366)
EARSM g2 (0.2189)
Experiment (0.3298)
CD in (brackets)

## Slide 19: URANS EARSM Horizontal Slice Streamwise Velocity
EARSM g1 (0.2366)
EARSM g2 (0.2189)
Experiment (0.3298)
CD in (brackets)

## Slide 20: Drag Coefficient: RANS and URANS, all grids
RANS and URANS much lower drag than LES/DES
SA is anomaly with high drag
EARSM has lowest drag
RKE
RSM
RSM and RKE similar

## Slide 21: RANS RSM + RKE Base Pressures
own g1 (0.2784)
own g3 (0.2540)
own g2 (0.2630)
CD in (brackets)
RSM
g1 (0.2597)
RKE
Experiment (0.3298)

## Slide 22: RANS RSM + RKE Horizontal Slice Streamwise Velocity
own g1 (0.2784)
own g3 (0.2540)
own g2 (0.2630)
CD in (brackets)
g1 (0.2597)
g1 (0.2597)
RKE
RSM
Experiment (0.3298)

## Slide 23: Drag Coefficient: RANS and URANS, all grids
Own grid
Low y+
SST
RANS and URANS much lower drag than LES/DES
SA is anomaly with high drag
EARSM has lowest drag
RSM and RKE similar
SST reasonably consistent

## Slide 24: RANS SST Base Pressures
own g2 (0.2753)
g2 (0.2783)
g2 (0.2492)
CD in (brackets)
own g2 (0.2809)
g2 (0.2478)
Experiment (0.3298)

## Slide 25: RANS SST Horizontal Slice Streamwise Velocity
own g2 (0.2753)
g2 (0.2783)
Experiment (0.3298)
CD in (brackets)
g2 (0.2492)
own g2 (0.2809)
g2 (0.2478)
Experiment (0.3298)

## Slide 26: Drag Coefficient: RANS and URANS, all grids
Own grid
Low y+
SA and variants
EARSM
SST
RKE
RSM
SA is anomaly with high drag
EARSM has lowest drag
RSM and RKE similar
SST reasonably consistent
RANS and URANS much lower drag than LES/DES

## Slide 28: Drag Coefficient: DDES and IDDES, all grids
DES

## Slide 29: Drag Coefficient: DDES and IDDES, all grids
DES
SA and variants
g1
g2
g3
IDDES
‘other’

## Slide 30: DDES and IDDES Base Pressures
own g2 (0.2803)
g2 (0.3131) IDDES
g2 (0.3322)
CD in (brackets)
own g2 (0.2906) ‘Other’
Experiment (0.3298)
SA

## Slide 31: DES and IDDES Horizontal Slice Streamwise Velocity
own g2 (0.2803)
g2 (0.3131) IDDES
Experiment (0.3298)
CD in (brackets)
g2 (0.3322)
own g2 (0.2906) ‘Other’
Experiment (0.3298)
SA

## Slide 32: Drag Coefficient: DDES and IDDES, all grids
DES
g1
g2
g3
g2
g3
own g1
own g2
SST

## Slide 33: DDES and IDDES SST Base Pressures
g2 (0.2792)
own g2 (0.2969)
g2 (0.2915)
CD in (brackets)
Experiment (0.3298)
SST
g3 (0.2900)
g3 (0.3118)

## Slide 34: DDES and IDDES SST Base Pressures
g2 (0.2792)
own g2 (0.2969)
Experiment (0.3298)
CD in (brackets)
g2 (0.2915)
Experiment (0.3298)
SST
own g2 (0.2969)
g3 (0.2900)
g3 (0.3118)

## Slide 35: Drag Coefficient: DDES and IDDES, all grids
DES
SA and variants
g1
g2
g3
‘other’
g1
g2
g3
g2
g3
own g1
own g2
SST
IDDES

## Slide 37: Drag Coefficient: LES, all grids
g1
g2
g3
own g3

## Slide 38: LES Base Pressures
g1 (0.2952)
g3 (0.3123)
g2 (0.3234)
CD in (brackets)
own g3 (0.3230)
Experiment (0.3298)
WALE
Vreman

## Slide 39: LES Horizontal Slice Streamwise Velocity
g1(0.2952)
g3 (0.3123)
Experiment (0.3298)
CD in (brackets)
g2 (0.3234)
own g3 (0.3230)
Experiment (0.3298)
WALE
Vreman

## Slide 40: Sideforce All

## Slide 41: Sideforce RANS and URANS
RANS too low sideforce

## Slide 42: Sideforce DDES/IDDES
DES high spread

## Slide 43: Sideforce LES
LES too high sideforce

## Slide 44: Lift All
Concerns about validity of experimental lift

## Slide 45: Lift RANS and URANS
RANS smallest downforce

## Slide 46: Lift DDES/IDDES

## Slide 47: Lift LES
LES highest downforce

## Slide 48: Roof Suction RANS and URANS

## Slide 49: Roof Suction DDES/IDDES

## Slide 50: Roof Suction LES

## Slide 51: Glasshouse LES

## Slide 53: Conclusion
Thanks to all contributors, very useful dataset, no major issues processing
Thanks to Astrid Walle for putting together the dashboard
Stronger conclusions than AutoCFD2
Three grids useful, and sensitivity is low
RANS gives incorrect flow structure: toroidal vortex with strong recirculation, generally too low drag (apart from SA)
DES/LES has correct flow structure with improved drag
  More consistency across submissions
  Consistency of drag prediction with base pressures and recirculation length
WM LES promising
  Two contributors consistent and good match to experiment