## Slide 1: TMY 2008 - 2017
10 km grid

## Slide 2
File | Description
UK_10kmgrid_kml | KML of grid points to use in Google Earth
UK_10kmgrid_info.xlsx | Table of xy and latlong of grid points
10kmgrid_2008_17_GHI_TMY.7z | Folder containing 2,453 csv files each with TMY irradiance (8760 hours)
INSTRUCTIONS:
Open the kml file in Google Earth or software of your choice and locate the grid point nearest to the location you are interested in. Look up the coordinates of the point in the grid info file. Unzip folder and use Windows Explorer to open the csv containing TMY data for your selected point.
See below for illustrated step-by-step example.

## Slide 3
Loughborough Example – Find the closest point using UK-10km_grid.kml
UK_10kmgrid_info.xlsx
- Find coordinates

## Slide 4
Unzip 10kmgrid-2008_17_GHI_TMY.7z and search for coordinates in Windows Explorer

## Slide 5
Month | Year
January | 2014
February | 2012
March | 2012
April | 2016
May | 2010
June | 2011
July | 2016
August | 2016
September | 2013
October | 2012
November | 2010
December | 2012
Loughborough Example (Point closest)

## Slide 6: Data Origins (1)
Data interpolated via ordinary kriging from 80+ UK Met. Office weather stations to 10 x 10 km grid.
Please cite the following:
Met Office (2006): MIDAS: Global Radiation Observations. NCAS British Atmospheric Data Centre, 8 August 2018 http://catalogue.ceda.ac.uk/uuid/b4c028814a666a651f52f2b37a97c7c7
Diane Palmer, Ian Cole, Tom Betts, Ralph Gottschalg, 2017, “Interpolating and estimating horizontal diffuse solar irradiation to provide UK-wide coverage: selection of the best performing models”, Energies, Special Issue “Solar Photovoltaics Trilemma: Efficiency, Stability and Cost Reduction 2017, 10, 181; doi:10.3390/en10020181 http://www.mdpi.com/1996-1073/10/2/181

## Slide 7: Data Origins (2)
The data available for download comprises hourly TMY Global Horizontal Irradiance values generated from the 2008-2016 decade for a 10 x 10 km resolution grid covering the UK and Northern Ireland. Global Horizontal Irradiance in Wh/m2.
The data is initially interpolated to each grid point from UK Meteorological Office measured weather station values. Ordinary kriging with an exponential semivariogram is used. The TMY for each point is then calculated as follows:
For each month in the year (i.e., Jan., Feb., March, etc.), the ten-year monthly mean of irradiance data is obtained for the period 2004-2015.
The historic month that most closely matches the ten-year mean for that month is identified i.e. the most “typical” month.
The hourly data values from the twelve typical months are combined to create the typical year file. This might comprise e.g. January from 2010, February from 2005, March from 2007 etc.
This simple method has been shown to perform well compared to other free-to-download TMY datasets.